## Slide 1: MATLAB EXERCISES
A DC signal of 10v is given for 100s . Plot in Matlab the sampled DC signal with fs=10 samples per sec. Use plot(t, x) MATLAB function to plot the output, where t contains sample point in time domain and x is the sampled DC signal. Use Matlab functions xlabel() and ylabel() appropriately.
A cosine signal of fm=10Hz and Am=10 is sampled with fs=200 samples per sec for 1 sec. Plot in Matlab the sampled cosine signal using both plot(t, x) and stem(t, x).
Repeat Q.2 with fs=100, 50, 20, and 10 samples per sec.

## Slide 2: MATLAB EXERCISES
Two cosine signals with fm1=10Hz, Am1=5 and fm2=50Hz, Am2=10 form a composite signal like
time domain is defined for Find the appropriate sampling frequency fs to plot the composite signal.
5. Repeat Q.4 with fs=500 samples per sec.

## Slide 3: MATLAB EXERCISES
6. For the signal x(t) shown
a) In Matlab, plot the function x(t) in the interval −5 ≤ t ≤ 5, using the plot function.
b) Construct the discrete-time sequence x[n] and use stem to plot it.
c) What is the suitable sampling frequency to avoid aliasing.